## Slide 1: Study for the computational resolution of conservation equations of mass, momentum and energy. Possible application to different aeronautical and industrial engineering problems: Case 1B
Author: Laura Pla Olea
Director: Carlos David Perez Segarra
Co-Director: Asensio Oliva Llena
Degree: Grau en Enginyeria en Tecnologies Aeroespacials
Delivery date: 10-06-2017 (Spring 2016-2017)
Notes: Good morning. I am Laura Pla Olea and I am going to present my study on the computational resolution of the conservation equations.

## Slide 2: List of contents
Objectives & Methodology
Conservation equations
Numerical methods
Basic cases
  Four materials problem
  Smith-Hutton problem
  Driven cavity problem
  Differentially heated cavity
  Burgers’ equation
Application ― Square cylinder
Conclusions
Future work

## Slide 3: Objectives
Provide knowledge in computational methods
Study of a specific case
Methodology
Basic cases
  Mathematical formulation
  Numerical method
  Code development
Specific application
Notes: What were the objectives of this work? Well, the main objective was to increase my knowledge in the field of the computational methods in order to solve the conservation equations. However, in order to summarize all the knowledge obtained, a second objective was to use these methods to solve a specific case.
To do so, the methodology was to begin solving some simple cases that required the use of numerical schemes. These cases would provide an introduction to different computational methods. For each case, the resolution began with the identification of the mathematical formulation needed to solve the problem. Then, a convenient discretization method was applied and, finally, a code was developed. At the end of the study, all this knowledge was applied to the specific case, following the same methodology

## Slide 4: Conservation equations
Describe heat transfer and fluid flow
No analytical solution
Particular cases of the generic convection-diffusion equation

## Slide 5: Numerical methods
Divide the domain ― Discretization
  Finite difference method
  Finite volume method
  Etc.
Space integration
Time integration
  Explicit:
  Implicit:
  Crank-Nicholson
P
W
E
S

## Slide 6: Four materials problem
 | ρ [kg/m3] | cP [J/kgK] | λ [W/mK]
M1 | 1500.00 | 750.00 | 170.00
M2 | 1600.00 | 770.00 | 140.00
M3 | 1900.00 | 810.00 | 200.00
M4 | 2500.00 | 930.00 | 140.00
Cavity wall | Boundary condition
Bottom | Isotherm at
Top | Uniform length
Left | In contact with a fluid at and
Right | Uniform temperature
Cavity wall | Boundary condition
Bottom | 
Top | 
Left | 
Right | 

## Slide 7: Four materials problem
Energy equation in a solid
Transient
Incompressible
No viscous dissipation

## Slide 8: Four materials problem ― Results

## Slide 9: Smith-Hutton problem

## Slide 10: Smith-Hutton problem
Generic convection-diffusion equation
Steady
Incompressible
Interpolation schemes
  Central differencing scheme (CDS)
  Upwind scheme (UDS)
  Exponential scheme (EDS)
  Hybrid scheme (HDS)
  Power-law scheme (PLDS)

## Slide 11: Smith-Hutton problem ― Results
Output for
Output for

## Slide 12: Driven cavity problem

## Slide 13: Driven cavity problem
Conservation of mass and momentum
Transient
Incompressible
Velocity Pressure

## Slide 14: Fractional Step Method
Explicit method
Helmholtz-Hodge decomposition theorem
  Momentum equation:
  Time integration:
  Intermediate velocity:
  Decoupling:
  Poisson equation:

## Slide 15: Fractional Step Method
Algorithm
  Evaluate
  Intermediate velocity
  Pressure
  Pressure correction

## Slide 16: Staggered meshes
To avoid unrealistic solutions
Three control volumes:
  Pressure
  Horizontal velocity
  Vertical velocity

## Slide 17: Driven cavity problem ― Results

## Slide 18: Driven cavity problem ― Results
Re = 100
Re = 1000
Re = 5000

## Slide 19: Differentially heated cavity

## Slide 20: Differentially heated cavity
Conservation of mass, momentum and energy
Transient
Incompressible (except the gravitational term)
Boussinesq approximation

## Slide 21: Differentially heated cavity ― Results

## Slide 22: Square cylinder
Inlet
Outlet
Walls

## Slide 23: Square cylinder
Conservation of mass and momentum
Transient
Incompressible

## Slide 24: Square cylinder ― Results
Re = 1
Re = 5
Re = 30
Re = 50

## Slide 25: Square cylinder - Results
Recirculation length
for

## Slide 26: Conclusions
Improved knowledge in numerical methods
  Discretization
  Interpolation schemes
  Fractional Step Method
  …
Realistic results
Application case: Square cylinder
  Steady solutions
  Accurate results

## Slide 27: Thank you
Questions?