## Slide 1: Study for the computational resolution of conservation equations of mass, momentum and energy. Possible application to different aeronautical and industrial engineering problems: Case 1B
Author: Laura Pla Olea
Director: Carlos David Perez Segarra
Co-Director: Asensio Oliva Llena
Degree: Grau en Enginyeria en Tecnologies Aeroespacials
Delivery date: 10-06-2017 (Spring 2016-2017)
Notes: Good morning. I am Laura Pla Olea and I am going to present my study on the computational resolution of the conservation equations.

## Slide 2: List of contents
Objectives & Methodology
Conservation equations
Numerical methods
Basic cases
  Smith-Hutton problem
  Driven cavity problem
  Differentially heated cavity
Application ― Square cylinder
Conclusions

## Slide 3: Objectives
Provide knowledge in computational methods
Study of a specific case
Methodology
Basic cases
  Mathematical formulation
  Numerical method
  Code development
Specific application
Objectives & Methodology
Notes: What were the objectives of this work? Well, the main objective was to increase my knowledge in the field of the computational methods in order to solve the conservation equations. However, in order to summarize all the knowledge obtained, a second objective was to use these methods to solve a specific case.
To do so, the methodology was to begin solving some simple cases that required the use of numerical schemes. These cases would provide an introduction to different computational methods. For each case, the resolution began with the identification of the mathematical formulation needed to solve the problem. Then, a convenient discretization method was applied and, finally, a code was developed. At the end of the study, all this knowledge was applied to the specific case, following the same methodology

## Slide 4: Conservation equations
Describe heat transfer and fluid flow
No analytical solution
Particular cases of the generic convection-diffusion equation
Conservation equations

## Slide 5: Numerical methods
Divide the domain ― Discretization
  Finite difference method
  Finite volume method
  Etc.
Space integration
Time integration
  Explicit:
  Implicit:
  Crank-Nicholson
P
W
E
S
Numerical methods

## Slide 6: Smith-Hutton problem
Basic cases – Smith-Hutton problem

## Slide 7: Smith-Hutton problem
Generic convection-diffusion equation
Steady
Incompressible
Interpolation schemes
  Central differencing scheme (CDS)
  Upwind scheme (UDS)
  Exponential scheme (EDS)
  Hybrid scheme (HDS)
  Power-law scheme (PLDS)
Basic cases – Smith-Hutton problem

## Slide 8: Smith-Hutton problem ― Results
Output for
Output for
Basic cases – Smith-Hutton problem

## Slide 9: Driven cavity problem
Basic cases – Driven cavity problem

## Slide 10: Driven cavity problem
Conservation of mass and momentum
Transient
Incompressible
Velocity Pressure
Basic cases – Driven cavity problem

## Slide 11: Fractional Step Method
Algorithm
  Evaluate
  Intermediate velocity
  Pressure
  Pressure correction
Explicit method
Helmholtz-Hodge decomposition theorem
Basic cases – Driven cavity problem

## Slide 12: Staggered meshes
To avoid unrealistic solutions
Three control volumes:
  Pressure
  Horizontal velocity
  Vertical velocity
Basic cases – Driven cavity problem

## Slide 13: Driven cavity problem ― Results
Re = 100
Re = 1000
Re = 5000
Basic cases – Driven cavity problem

## Slide 14: Differentially heated cavity
Basic cases – Differentially heated cavity

## Slide 15: Differentially heated cavity
Conservation of mass, momentum and energy
Transient
Incompressible (except the gravitational term)
Boussinesq approximation
Basic cases – Differentially heated cavity

## Slide 16: Differentially heated cavity ― Results
Basic cases – Differentially heated cavity

## Slide 17: Square cylinder
Inlet
Outlet
Walls
Application – Square cylinder

## Slide 18: Square cylinder
Conservation of mass and momentum
Transient
Incompressible
Application – Square cylinder

## Slide 19: Square cylinder ― Results
Re = 1
Re = 5
Re = 30
Re = 50
Application – Square cylinder

## Slide 20: Square cylinder - Results
Recirculation length
for
Application – Square cylinder

## Slide 21: Conclusions
Improved knowledge in numerical methods
  Discretization
  Interpolation schemes
  Fractional Step Method
  …
Realistic results
Application case: Square cylinder
  Steady solutions
  Accurate results
Conclusions

## Slide 22: Thank you
Questions?